## Slide 1: ENGI 301 One-Handed Piano Project Proposal
10/01/2023
Shannon McGill

## Slide 2: Background Information
My one-handed piano will teach beginner pianists how to play simple songs through memorization and repetition of a light sequence.
  Lights corresponding to a given key will illuminate in a given sequence.
  Users will press the correct buttons in the correct order to play a simple song.
  Why? I love memorization games, and I have always wanted to learn to play the piano. This is a perfect combination of the two!
My project will be a (much) simplified version of this piano that requires you to memorize the light sequence to learn the song!

## Slide 3: Background Information
Existing Projects Leveraged (Hyperlinked)
  Whac-a-Mole Game with PocketBeagle shows how to illuminate lights in a certain order.
  PocketBeagle Synthesizer will help me in learning how to sync buttons with specific notes.
  Music Box uses USB speakers to play music and includes the LCD screen I plan to use.
My project will combine aspects of the above projects to display lights in a given sequence that will correspond to the buttons to press to play a song on my piano.
Whac-a-Mole Game with PocketBeagle
PocketBeagle Synthesizer
Music Box

## Slide 4: System Block Diagram
LCD Touchscreen
ILI9341
5 GPIO.IN (P1.26, P1.28, P1.30, P1.32, P1.34)
SPI1
PocketBeagle
USB1
Buzzer
Product ID: 1536
I2C1
Resistive Touch Screen Controller
Product ID: 5423
PWM1A
Arcade Buttons
ASIN: B01N11BDX9
USB Speaker
LLR050A

## Slide 5: Power Block Diagram
LCD Touchscreen
ILI9341
5 GPIO.IN (P1.26, P1.28, P1.30, P1.32, P1.34)
SPI1
PocketBeagle
USB1
Buzzer
Product ID: 1536
I2C1
Resistive Touch Screen Controller
Product ID: 5423
PWM1A
Arcade Buttons
ASIN: B01N11BDX9
USB Speaker
LLR050A
5V (not from PocketBeagle), current unknown
5V, 5-10 mA
3.3 V, max 5 mA
3.3 V, max 50 mA
3.3 V, max 150 mA

## Slide 6: Components / Budget
Component (Components to Purchase are Hyperlinked!) | Need to Buy | Cost
Arcade LED Buttons | Yes | $11.88
Transistors for LEDs* | Yes | TBD
Resistors | No | N/A
USB Speaker | Yes | $15.98 (On Sale!)
USB Adapter | No | N/A
SPI Screen | Yes | $29.95
Resistive Touch Screen Controller | Yes | $4.95
Buzzer | No | N/A
*Professor Welsh will choose which transistors to buy and I will update this list accordingly.