## Slide 1: ENGI 301 PCB Project
Shannon McGill
Due 12/12/2023 @ 11:59pm

## Slide 2: Background Information
Create a PCB for a “One-Handed Piano”
Hardware:
  Five Arcade Buttons (Keys)
  SPI Display Screen (Game Interface)
  USB Adapter (Speaker)
  Buzzer (Incorrect Notes)
  Five Transistors
  Fifteen Resistors

## Slide 3: System Block Diagram – “One-Handed Piano”
LCD Touchscreen
ILI9341
10 GPIO (P2.1, P2.3, P2.5, P2.7, P2.9 for LEDs, P2.2, P2.4, P2.6, P2.8, P2.10 for buttons)
SPI1, including power, ground, and 2 GPIO (P2.17, P2.19, P2.21, P2.23, P2.25, P2.27, P2.29, P2.31)
PocketBeagle
USB1 (P1.7, P1.9, P1.11, P1.13)
Buzzer
Product ID: 1536
Arcade Buttons
ASIN: B01N11BDX9
USB Speaker
LLR050A
PWM1A (P 1.36)
Note: LED is wired as a transistor-controlled LED, and the button is wired in the active high configuration. They are both powered by 5 V.

## Slide 4: Mechanical Drawing
FRONT
BACK
Pocket Beagle
microUSB
Buzzer
USB Adapter
SPI Screen
3.3”
2.6”
Note: The colored boxes represent the colored buttons and their associated resistors and transistor.